Rot setzt aus (klopfempfindlich). IC1001 (M52721SP) nachlöten. Position: Bildröhrenplatte x=33mm, y=45mm.

Unterschied zwischen dem Modell 108010 und dem Modell 108015. Unterschiede in der Ergonomie: 
108010 (TX-D2171XD-E/M-2171XD-E ): MPRII und TCO92 
108015 (M-1F71XD-ET) TCO95

Kein Funktion. LED leuchtet nicht. C855 (2200uF/25V) prufen.

Keine Funktion. Q890 (SMD NPN Uni), C828 (47uF/63V),C829 (4,7uF/63V),C824 (47uF/63V) und C822
(330uF/63V) haben Unterbrechung oder Teilkapazitätsverlust.

OSD Erscheint, jedoch funktionieren nur die rechten drei Tasten,. Keine Einstellungen möglich. D106 (DTZ5A6B) 5,6V Z-Diode am Prozessorboard defekt. Position: Prozessorboard x=15mm, y=20mm neben eingelöteten Stecker N1015B.

Fokus-Abgleich nach dem Wechsel des Hochspannungstrafos. RemedyRichtige Vorgehensweise: Benutzung der Hersteller-Software: 
Nur für eigene Forschungszwecke kann alternativ folgende Methode verwendet werden: Leitung DACg51 (stat. Fokus) am Pin 3 des D/A-Wandler IC541 auftrennen und von dieser Leitung einen Einstellregler 50K gegen Masse schalten.
Bei Notwendigkeit kann auf gleiche Weise auch Einstellung des dynamischen Fokus (Pin 2 des IC541) oder andere Einstellungen vorgenommen werden.

Hochspannngsteil taktet. D541 (MA4150 15V Zenerdiode) hat Schluss. Zusätzlich kann Sicherung Q876 (UN11008) Unterbrechung haben.

Bezeichnung der Diode D541. D541 = MA4150M

Bild wird zeitweise sehr unscharf. DST tauschen.

Beim Einschalten stirbt Zeilenendstufentransistor (2SC5243) gleich. Transistor Q873 wechseln.

BNC-Eingang geht nicht. Zenerdiode D231 (MA8056) im H-Sync. Eingang des Monitors hat Kurzschluss. Kann mit handelsüblicher Zenerdiode 5V6 ersetzt werden.

LED blinkt, keine Funktion. Sicherung Q674 (TR5/800mA) ist defekt. ZTR prüfen.

Hochspannung fehlt beim Einschalten und die Netzteil-LED blinkt. Die Netzteilplatine komplett nachlöten, besonders auf die 'dicken' Dioden und deren Durchkontaktierungen achten.

Bild ist flau. Kontrast und Luminanz sind regelbar. Prüfen, ob alle 6 SMD Abschlusswiderstände am BNC und am SUB-D Eingang vorhanden sind.

Fokusabgleich ohne Software. Abgleich ist auch ohne Software möglich, aber nur bei Geräten mit ovalen Tasten. Diese halten und warten bis Entmagnetisierung abschaltet. Geraet wieder ausschalten und Prozedur wiederholen. Jetzt ist im Onscreen-Menue, Position unten rechts ein Menuepunkt Fokus sichtbar. Mit Taste 2 kann zwischen V-und H-Fokussierung umgeschaltet werden, mit Pfeil links rechts abgleichen. Geraet ausschalten, dann werden die Werte gespeichert.

Kein Bild. Ablenkung ist ok. [Hochspannung ist vorhanden]. Widerstand R652 (100R/0,2W) ist defekt. Evtl. hat sich die Bildröhrenleiterplatte beim Transport gelöst. Es wird bei diesem Gerät mittels Klemmschraube am Bildröhrenhals und nicht mittels Schaumstoffkissen festgehalten.

Gerät geht unregelmässig aus. [Schutzschaltung, -16V für Vertikalendstufe werden abgeschaltet].
Durchkontaktierung Masseverbindung R838 ist schlecht.

Keine Hochspannung. Netzteil versucht hoch zu fahren. Q550 hat Schluß. Ablenktransistor Q 550 (2SC5243), Q873 (2SJ306) und IC-Sicherung Q876 wechseln. Ursache schlechte Lötstelle am Ablenkstecker. Q873 befindet sich am oberen Rand der stehenden Platine. Die Sicherung 2-3cm darunter.

Fokusabgleich ohne Software. Abgleich geht auch ohne Software, aber nur bei Geräten mit ovalen Tasten. Tasten 1+2 drücken und halten. Halten und warten bis Entmagnetisierung abschaltet. Gerät wieder ausschalten und Prozedur wiederholen. Jetzt ist im On-screen Menü, Position unten rechts ein Menüpunkt Fokus sichtbar. Mit Taste 2 kann zwischen V-und H-Fokussierung umgeschaltet werden, mit Pfeil links rechts abgleichen. Geraet ausschalten, dann werden die Werte gespeichert.

Kein Bild. [Keine Hochspannung, H-Ablenkung ok]. Wenn Sicherung Q674 defekt ist, muss FBT gewechselt werden (TLFA00965). Ansonsten folgende Lötstellen, bzw. Verbindungen prüfen (Leiterplatte, Lötseite, Digiboard oben): Netztrafo Pin 3 (obere Reihe, 3. von links) zu Anode D855; Kathode D853 nach L863; Kathode D856 nach Q858/E (an Kühlblech oberhalb Trafo rechts vom Trennstrich); Spule L860 nach R850 (kurz oberhalb Trafo); Q856/E (links unterhalb Digiboard) nach R897 und R899 (weiter schräg links unten).

Remedy No. 2Alle NT-Dioden sekundär nachlöten (viele kalte Lötstellen, trotz doppelseitige Platine) und evtl. Brücken ziehen von ( NT 
Sekundär). Platine mit Lötseite oben und 220V-Buchse links vor einer Brücke. Sperrwandlertrafo 3. Pin von oben rechts auf Anode D855 / Brücke Kathode D853 zur Spule L863 / Brücke L860 rechts zum Widerst. R850 links / Brücke Q856 linkes Bein ( 2cm links neben Digiboard ) zur Mitte zwischen R897 und R899 ( links oben darüber )

Bild wird zeitweise sehr unscharf. DST tauschen.

Keine Funktion. Netzteil startet nicht. R826 (470K/0,5W) MEO hochohmig.

Fokusabgleich ohne Software. Abgleich geht auch ohne Software, aber nur bei Geräten mit ovalen Tasten. Halten und warten bis Entmagnetisierung abschaltet. Gerät wieder ausschalten und Prozedur wiederholen. Jetzt ist im On-screen Menü, Position unten rechts ein Menüpunkt Fokus sichtbar. Mit Taste 2 kann zwischen V-und H-Fokussierung umgeschaltet werden, mit Pfeil links rechts abgleichen. Geraet ausschalten, dann werden die Werte gespeichert.

Vorwiegend nach Kaltstart keine Heligkeit, Hochspannung und Ablenkungen in Ordung. Es liegt eine Unterbrechung im Heizkreis vor. Die Leiterplattendurchkontaktierungen zwischen Emmiter Q858 und R856 ayf dem Main Board (Netzteil - Chassis) nacharbeiten.

Technische Daten. Bildröhre: 21 Zoll Multifrequenz
Lochmaske: 0,25mm
Horizontalfrequenz: 30-115kHz
Vertikalfrequenz: 50-160Hz
Video Bandbreite: 250MHz
Vertikalfrequenz:
640x480 max. 160Hz
800x600 max. 160Hz
1024x768 max. 140Hz
1280x1024 max. 105Hz 
1600x1200 max. 90Hz Max. Auflösung

Netzteil startet nicht. Feler 1: Kalte Lötstellen an der Anode von D855.

Remedy No. 2Netzteil nachlöten.

Q674 (0,8A), Halbleitersicherung im Hochspannungsteil löst aus. [Kein Schluss feststellbar].
DST ist defekt.

Kein Bild, keine Hochspannung, H-Ablenkung ok. Wenn Sicherung Q674 defekt ist, muss FBT gewechselt werden (TLFA00965). Ansonsten folgende Lötstellen, bzw. Verbindungen prüfen (Leiterplatte, Lötseite, Digiboard oben): Netztrafo Pin 3 (obere Reihe, 3. von links) zu Anode D855; Kathode D853 nach L863; Kathode D856 nach Q858/E (an Kühlblech oberhalb Trafo rechts vom Trennstrich); Spule L860 nach R850 (kurz oberhalb Trafo); Q856/E (links unterhalb Digiboard) nach R897 und R899 (weiter schräg links unten).

Fokusabgleich ohne SoftwareAbgleich geht auch ohne Software, aber nur bei Geräten mit ovalen Tasten. halten und warten bis Entmagnetisierung abschaltet. Geraet wieder ausschalten und Prozedur wiederholen. Jetzt ist im Onscreen-Menue, Position unten rechts ein Menuepunkt Fokus sichtbar. Mit Taste 2 kann zwischen V-und H-Fokussierung umgeschaltet werden, mit Pfeil links rechts abgleichen. Geraet ausschalten, dann werden die Werte gespaeichert.

Kein Bild. LED grün. [107V Gleichspannung an H-Ablenkstufe fehlt. Ansteuerung fehlt]. Treibertrafo T541 und Basis Q550 nach kalte Lötstellen prüfen.

Kein Bild. LED grünHalbleitersicherung Q876 (UN11008) ist unterbrochen. Transistor Q550 (2SC5243) prüfen.

No raster. Check flyback transformator pin 3 B+, if abnormal check power supply unit.

Remedy No. 2Check HV operation, if abnormal check horizontal oscillator, horizontal deflection, HV circuit.

Remedy No. 3Check CRT filament voltage 6.3V, if abnormal check power supply unit.

Remedy No. 4[Filament not lit]. Replace CRT socket or CRT.

Remedy No. 5Turn screen variable resistor to right.

Remedy No. 6Check screen (G2) voltage (range: 450 to 700V), if too low check G2 wire to video PCB disconnect, replace FBT T402 and CRT.

Remedy No. 7Check video B+ (85V).

Abnormal video on CRT screen.

Measure R.G.B. video output at pins 2, 5 and 7 on CRT socket, if abnormal check B+ 85V.

Remedy No. 2[B+ 85V abnormal]. Check power supply unit.

Remedy No. 3Check video post-amp, if abnormal then cascade circuit failure, replace Q902, Q903, Q904, Q905, Q907 and Q908.

Remedy No. 4Check video pre-amp IC901, pin 9 blanking, pin 10 clamp.

Remedy No. 5Check pin 6 of IC901 DC range (1 to 6V), if abnormal then replace IC901 (TDA4882).

Remedy No. 6Check in/out cable input.

Remedy No. 7[RGB video output at pin 2, 5 and 7 on CRT socket V901 normal]. Turn screen variable resistor clockwise, check screen voltage range (450 to 700V), if too low then G2 wire to video PCB disconnect, replace FBT T402 failure and CRT.
 Abnormal white balance. Re-adjust white balance, VR901, VR902 and VR903.

Remedy No. 2Re-adjust white balance. Also check IC901 pin 9 blanking, pin 10 clamp.

Remedy No. 3Check pin 6 of IC901 DC range (1 to 6V).

Remedy No. 4Replace IC901, VR904, VR905 and associated circuit.

No blanking. Check horizontal blanking on video board, pin 9 of IC901 blanking, if normal replace IC901.

Remedy No. 2[Horizontal blanking on video board pin 9 of IC901 blanking abnormal]. Check pin 2 of IC401 , if abnormal check pin 7 of T402.

Remedy No. 3[Pin 7 of T402 normal]. Replace IC401.

Remedy No. 4[Pin 7 of T402 abnormal]. Check for raster or FBT failure.

Remedy No. 5Check vertical blanking on video board IC901 clamp, if normal then replace IC901.

Remedy No. 6Check pin 8 of IC401 clamp, if normal replace IC401.

Remedy No. 7[Pin 8 of IC401 clamp abnormal]. Check Q307 collector, if normal then replace Q307 and ZD302.

Remedy No. 8[Q307 collector abnormal]. Check pin 8 of IC301.

Remedy No. 9Replace IC301.

Horizontal oscillator/deflection/HV circuit failure. Check HV protector for operation, if normal check horizontal driver/output.

Remedy No. 2[Horizontal driver/output abnormal]. Replace IC401 and associated circuit.

Remedy No. 3[Horizontal driver/output normal]. Replace D409, D413, Q406 and D403.

Remedy No. 4[HV protector operation abnormal]. Replace HV protector, ZD401, R418, R421 and switch power.

F/V converter and unstable synchronization. Check horizontal sync on main board pin 9 of IC401, if abnormal check in/out cable horizontal sync input on video board P901.

Remedy No. 2Check C405 voltage, if abnormal then re down load, if not OK then replace IC102, Q419 and Q423.

Remedy No. 3Adjust VR401.

Remedy No. 4Check IC401.

Remedy No. 5Check vertical sync on main board pin 10 of IC401, if abnormal check in/out cable vertical sync input on video board P901.

No power management functionCheck indicator LED (LD401) colour.

Remedy No. 2Check Q101 active low.

Remedy No. 3Check pin 13 of IC101 active low, re down load, replace IC101.

Remedy No. 4Check Q302 and Q809 active low.

Remedy No. 5Check pin 15 of IC101 active low, re down load, replace IC101.

No OSD function. Check voltage (5V) on pin 9 of IC903, if abnormal, check R976 and ZD902.

No display data channel 1. Check display data channel 1.

Remedy No. 2Read IC2 data, if abnormal, check pins 5 and 7 of IC902, TTL, if abnormal, check P901 vertical sync data.

Remedy No. 3Reset, if not OK then IC902 or DDC1/2B card failure.

Horizontal F/V adjustment.

ProcedureL
1. Apply 75.12KHz signal.
2. Adjust VR809 (H F/V) until voltage at V19 (pin 19 of IC801) or TP806 is 4.82V (+/-0.01V).
3. Adjust VR807 until voltage at V48 (pin 48 of IC801) or TP805 is 5.55V (+/-0.01V).
4. Apply 53.57KHz signal.
5. Adjust VR808 until voltage at V48 (pin 48 of IC801) or TP805 is 8.85V (+/-0.01V).
6. Repeat steps 2 to 5 until specified is attained.
7. Apply 75.12KHz signal. 
8. S/C pin 8 of IC801and +B. 
9. Adjust horizontal hold VR810 until frequency is 75.12KHz (+/-20Hz) with a frequency counter.

Vertical F/V adjustment.

Procedure:
1. With only synchronizing signal being absent, adjust vertical hold 1 VR801 until vertical scanning frequency is 35Hz ±1Hz.
2. Apply 60Hz signal. 
3. Adjust vertical F/V VR804 until voltage at source of Q86 is 4.12V ±0.01V.

VGA mode adjustment.

Procedure:
1. Apply 51KHz signal. 
2. Turn VR202 clockwise until voltage at TP205 or pin 13 of CN802 begins changing higher.
3. Apply 31.5KHz signal.
4. Adjust VR806 until voltage at VR48 (pin 48 of IC801) or TP805 is 5.18 (+/-0.01V).

Pulse timing adjustment. Procedure:
1. Adjust VR201 until pulse width at pin 2 of CN22a, pin 3 of CN403 or TP201 is 1us.
2. Adjust VR803 until pulse width at pin 10 of IC802 or TP808 is 0.38ms.

Horizontal drive adjustment. Procedure:
1. Apply 75.12KHz signal.
2. Adjust VR215 to minimum power consumption position.
3. Turn VR215 clockwise until power consumption increases to 2W against minimum power consumption.

CRT cut-off adjustment. Procedure:
1. Set VR217 until voltage at FB503 on CRT socket board is -5V.
2. Set VR402R, G, B to minimum.
3. Set SW202 on main board to service position.
4. Adjust RGB VR402 without most high light colour using FBT screen variable resistor until horizontal line on screen is barely visible.
5. Set service switch (SW22) back to operate position.

Bright horizontal line appears on screen. Check voltage (50Vpp) on pin 5 of IC430, if normal, check deflection yoke.

Remedy No. 2[Voltage on pin 5 of IC430 abnormal]. Check voltage on pin 1 of IC430, if abnormal check IC430 and +16V/-16V line.
 Remedy No. 3Check SSP card.

Incorrect V.PCC and horizontal size[Voltage (3.1V) on pin 1 of IC850 abnormal]. Check voltage (2.5V) on pin 9 of IC8001, if abnormal, check pins 4 and 5 of IC541.

Remedy No. 2[Pin 9 of IC8001 voltage normal]. Check IC8001, Q8001 and Q8002.

Remedy No. 3[Voltage (0.1Vpp) on pin 1 of IC850 abnormal]. Check voltage (5.2Vpp) on pin 13 of IC8001, if abnormal check SSP card.

Remedy No. 4[Pin 13 of IC8001 voltage normal]. Check IC8001, Q8001 and Q8002.

Remedy No. 5Check IC850.

Incorrect horizontal position control[Raster position centre]. Check SSP card.

Remedy No. 2Check voltage (17.5V) on pins 3, 4, 5 of IC581, if abnormal check D580 and D581.

Remedy No. 3Check voltage (7.1V) on pins 1, 2, 3 of IC581, if normal check IC581.

Remedy No. 4[Pins 1, 2 and 3 of IC581 voltage abnormal]. Check voltage (10.2V) on pin 1 of IC582, if abnormal check IC582.

Remedy No. 5Check voltage (2.8V) on pin 3 of IC583, if abnormal check pin 11 of IC541.

Remedy No. 6Check IC583 and Q580.

Incorrect vertical position controlCheck voltage (1.2V on pin 7 of IC430), if abnormal check pin 10 of IC541.
Print this repair tip | Feedback

Remedy No. 2Check IC430.

Incorrect vertical size. Check voltage (50Vpp) on pin 5 of IC430, if normal check deflection yoke.
Print this repair tip | Feedback

Remedy No. 2[Pin 5 of IC430 voltage abnormal]. Check voltage (1.1Vpp) on pin 1 of IC430, if abnormal, check SSP card.
Print this repair tip | Feedback

Remedy No. 3Check IC430 and +16/-16V line.

No OSD. [Voltage (5Vpp) on pin19 of IC1101 normal]. Check voltage (4Vpp) on pin 20 of IC1101, if abnormal check IC1405.
Print this repair tip | Feedback

Remedy No. 2[Pin 20 of IC1101 voltage normal]. Check IC1101.
Print this repair tip | Feedback

Remedy No. 3[Pin 19 of IC1101 voltage abnormal]. Check voltage (5Vpp) on pin 5 of IC1405, if abnormal, check SSP card, N1013 (20).
Print this repair tip | Feedback

Remedy No. 4Check voltage (5Vpp) on pin 10 of IC1405, if abnormal, check SSP card, N1013 (18).
Print this repair tip | Feedback

Remedy No. 5Check voltage (5Vpp) on pins 7 8 of IC1405, if abnormal, check SSP card, N1013 (25) (26).
Print this repair tip | Feedback

Remedy No. 6Check IC1405.

Defective horizontal deflection circuit. [Q550 (C) voltage (500Vpp) normal]. Check deflection yoke.
Print this repair tip | Feedback

Remedy No. 2[Q550 (C) voltage (500Vpp) abnormal]. Check voltage (125.5V) on T542 (P4).
Print this repair tip | Feedback

Remedy No. 3[T542 (P4) voltage abnormal]. Check voltage (195V) on Q873 (S), if normal, check voltage (200Vpp) on Q873 (G).
Print this repair tip | Feedback

Remedy No. 4[Q873 (G) voltage normal]. Check Q873.
Print this repair tip | Feedback

Remedy No. 5[Q873 (G) voltage abnormal]. Check voltage (1Vpp) on Q870 (B), if abnormal, check IC850.
Print this repair tip | Feedback

Remedy No. 6[Q870 (B) voltage normal]. Check Q870, Q871 and Q872.
Print this repair tip | Feedback

Remedy No. 7[T542 (P4) voltage normal]. Check voltage (7Vpp) on Q550 (B), if normal, check Q550.
Print this repair tip | Feedback

Remedy No. 8[Q550 (B) voltage abnormal]. Check voltage (21V) on T541 (P1), if abnormal check voltage (27.5V) on pin 5 of IC540.
Print this repair tip | Feedback

Remedy No. 9[Pin 5 of IC540 voltage abnormal]. Check 28V line.
Print this repair tip | Feedback

Remedy No. 10[Pin 5 of IC540 voltage normal]. Check voltage (7.1V) on pin 2 of IC540, if abnormal, check pin 1 of IC541.
Print this repair tip | Feedback

Remedy No. 11[Pin 2 of IC540 voltage normal]. Check IC540 and R540.
Print this repair tip | Feedback

Remedy No. 12[T541 (P1) voltage normal]. Check voltage (56Vpp) on T541 (P2), if normal, check T541.
Print this repair tip | Feedback

Remedy No. 13[T541 (P2) voltage abnormal]. Check voltage (10Vpp) on Q540 (G), if normal, check Q540.
Print this repair tip | Feedback

Remedy No. 14[Q540 (G) voltage abnormal]. Check Q535 and Q536 (B), if abnormal check SSP card.

No power. Check voltage 195V line, if normal then abnormal power saver.
Print this repair tip | Feedback

Remedy No. 2[195V line abnormal]. Check pin 2 of T801, if no B+ check D808 (2) (30AC).
Print this repair tip | Feedback

Remedy No. 3[D808 (2) (30AC) abnormal]. Check AC fuse and AC input.
Print this repair tip | Feedback

Remedy No. 4[D808 (20 (3) AC normal]. Check D808.
Print this repair tip | Feedback

Remedy No. 5Check voltage (24.5V) on pin 4 of IC820, if no Vcc check Q820 (C).
Print this repair tip | Feedback

Remedy No. 6[Q820 (C) correct]. Check Q820, Q890 and pin 9 of IC820.
Print this repair tip | Feedback

Remedy No. 7[Q820 (C) incorrect]. Check R820 and R827.
Print this repair tip | Feedback

Remedy No. 8Check voltage (0.3V) on pin 8 of IC820, if abnormal check R811, R812, R819, D805 and pin 9 of IC820.
Print this repair tip | Feedback

Remedy No. 9Check IC820 and secondary.

Abnormal power saver. [Voltage on pins 20 and 21 of N1015A (0V), Pin 22 of N1015A (5V)]. Check power saver.
Print this repair tip | Feedback

Remedy No. 2Check voltage (4.2Vpp) on pin 8 of N1013A, if abnormal check voltage (2.5Vpp) on pin 6 of IC280.
Print this repair tip | Feedback

Remedy No. 3[Pin 6 of IC280 voltage normal]. Check IC281.
Print this repair tip | Feedback

Remedy No. 4[Pin 6 of IC280 voltage abnormal]. Check voltage (5Vpp) on pin 11 of IC1331, if normal check IC280.
Print this repair tip | Feedback

Remedy No. 5[Pin 11 of IV1331 voltage abnormal]. Check voltage (5Vpp) on pin 12 of IC1331 if normal check IC1331.
Print this repair tip | Feedback

Remedy No. 6Check voltage (5Vpp) on pin 12 of N1013A, if abnormal check voltage (2.5Vpp) on pin 8 of IC280, if normal check IC280.
Print this repair tip | Feedback

Remedy No. 7[Pin 8 of IC280 voltage abnormal]. Check voltage (5V) on pin 3 of IC1331, if normal check IC1331.
Print this repair tip | Feedback

Remedy No. 8[Pin 3 of IC1331 voltage abnormal]. Check pin 2 of IC1331 voltage (5V), if normal check IC1331.
Print this repair tip | Feedback

Remedy No. 9Check SSP card.